## Slide 1: Towards An Early Design Space Exploration Tool Set for STT-RAM Design
Philip Asare and Ben Melton

## Slide 2: STT-RAM Overview: Advantages
Everything volatile currently has
  High speed (SRAM)
  Density (DRAM)
AND Everything non-volatile presents
  Non-volatility
  Low Power (Flash)
  Reliability (Hard-drive)
On its own
  CMOS-compatible
  Good scalability potential (over tradition MRAM)
Potential for use as universal memory

## Slide 3: STT-RAM Overview: Challenges
Device-Level
  Tunneling Magneto-Resistance Ratio (TMR)
  Fabrication Issues
Circuit-Level
  Current-sensing
  Variation
    cell strength: reading difficulty
    sense amp: offset (especially at smaller nodes)
  Stochastic nature of MTJ
Architecture-Level
  Read-write asymmetry in energy and delay
  Periphery components may dominate

## Slide 4: Road Map
STT-RAM Overview
  Advantages
  Challenges
Requirements for Addressing Challenges
Our Approach to Addressing Challenges
  Understanding STT-RAM
  Experimental Setup
Results + Insights
Future Work + Summary

## Slide 5: Addressing STT-RAM Challenges
Requires cross-layer design
  Layers of abstraction can get in the way
  Need to know impact of decisions across layers
  Need ‘generic’ way of doing this
Tools available for cross-layer design (from SRAM)
  Technology Agnostic Simulation Environment (TASE)
    Process-to-Circuit-Level Interface
    One simulation template different PTMs
  Virtual Prototyper (ViPro)
    Circuit-to-Architecture-Level Interface
    Circuit-level decisions on Arch-level and vice versa
    Can work on TASE output to provide full cross-layer view
Our Approach: Extend TASE + ViPro Concept for STT-RAM

## Slide 6: Understanding STT-RAM: Structures
Storage Element*
MTJ Resistance Characteristics*
Bit Cell and Column
Array
* A. Nigam et al., “Delivering on the Promise of Universal Memory for Spin Torque Transfer RAM (STT-RAM)” International Symposium on Low-Power Electronics and Design (ISLPED), August 2011

## Slide 7: Understanding STT-RAM: Read
(1)
(2)
(1)
Decode address  select word
Turn on sense amp  pre-charge BL
Disable precharge  evaluate/read data
Turn off sense amp
(1)
(2)
(1)
X
X
X
(3)
(4)
(2)

## Slide 8: Understanding STT-RAM: Write
(1)
(1)
Decode address  select word
Charge BL or SL to write (depends on value)
Disable write transistors
(1)
(2) or X
(2)
(3)
(3)
X or (2)
(2) or X
X or (2)

## Slide 9: Experimental Setup
Independent Variables
  Process Level: Technology PTM
  Circuit-Level: VDD, W (of access transistor)
  Array-Level: Capacity, # Rows , Word size
Dependent Variables
  Energy: Read and Write (FOM)
  Delay: Read and Write (FOM)
  Associated intermediate variables (e.g. bit cell write time)

## Slide 10: Experimental Setup
Experimental Workflow
  Simulations
    TASE
      For each PTM, vary VDD+W
      Collect currents (read +write)
    HSPICE
      Collect sense amp info (current, delay, Vread f(V))
  ViPro (Analytical Modeling and Virtual Prototyping)
    use TASE output to calculate intermediate variables
    compute FOMs based on analytical models

## Slide 11: Results: Bit Cell Analysis
Setup
  Iwrite-V Curve
General Results
  Current increases with voltage
  Current increases with node size

## Slide 12: Results: Array-Level Decisions
Setup
  Fixed Capacity (1MB)
  Fixed VDD=0.9V, W=22nm (22nmPTM)
  Varied #rows and word size
General Results
  E, D write > read
  D read ~ x1ns
  D write ~ x10ns
  E read, write < 1pJ
  E, D more sensitive to wordsize

## Slide 13: Results: Circuit-Level Decisions
Setup
  Fixed array structure
  Vary VDD and W (22nm PTM)
General Results
  Energy increases with VDD
  Delay decreases with increased VDD

## Slide 14: Results: Circuit-Level Decisions
Setup
  Fixed array capacity
  Vary VDD and W (22nm PTM)
General Results
  Width has little effect on energy

## Slide 15: Results: Process-Level Decisions
Setup
  Fixed array structure
  Fix VDD=nominal for PTM, W=2Wmin
  Vary PTM
General Results
  PTM has more effect on energy
  E,D increases with node size
  *Note: write delay artifact of model

## Slide 16: Insights
Majority of energy consumed in periphery
  Decoders, Sense Amps
Cross-layer view better for optimization
  Difficult to do without tools like TASE and ViPro
STT-RAM modeling and design is still in its infancy
  Few good models available
  Available models inconsistent from one to the other
  Three distinct perspectives
    Process, circuit, and architecture with nothing in between
    Tough to reconcile perspectives

## Slide 17: Future Work + Summary
Future
  Improve STT-RAM Models!!!
    Requires more research and understanding
    We made a lot of assumptions
  Extend tools for more comprehensive analysis
  Integrate tools better (minor implementation issue)
    We did a lot of manual ‘gluing’
Summary
  STT-RAM has the potential to shake the memory industry
  Challenges in design need to be overcome
  Cross-layer design perspective required
  We showed this can be done